## Slide 1: IHI’s Biomass Firing Technologies and Solutions toward a Low-Carbon Society
Biomass Seminar organized by JCOAL
12th May 2026
Basic Design Gr. Life Cycle Management Dept.
Carbon Solution Business Unit
Resources, Energy & Environment Business Area
IHI Corporation
JL. Raya Bojonegara-Salira, Argawana
Puloampel, Serang, Banten, Indonesia 42454
PT IHI POWER SERVICE INDONESIA

## Slide 2: Table of Contents
Introduction of IHI Corporation and IHI Group
Indonesia Government & Utility Biomass Policies
Biomass (Co-)Firing Technologies
Design Consideration for Biomass (Co-)Firing

## Slide 3: 1. Introduction of IHI Corporation
Domestic base
Resources, Energy &
Environment
Industrial Systems &
General-Purpose Machinery
Aero Engine,
Space & Defense
Social Infrastructure
4 Areas of expertise
IHI is a global company with 30 overseas bases and presence in 22 countries

## Slide 4: 1. Introduction of IHI Power Service Indonesia
Overview of PT IHI Power Service Indonesia (IPSI)
Company Name: PT IHI Power Service Indonesia
Shareholders: IHI(88.76%), Jurong Engineering Limited(11.24%, IHI Gr company)
Date of Incorporation: 17 March 1984 Services: Steel Structure & Heavy Equipment, Boiler Pressure Parts, Piping,
Static Equipment, Life Cycle Business.
Location: Banten, Indonesia (approx.100km west from Jakarta)
Non-Pressure Parts (4 Shops)
Steel Structure, Container Crane, Stacker Reclaimer, etc.
Facilities :
CNC cutting, drilling machine, rolling machine,
bending machine, etc.
Pressure Parts ((6 Shops)
Boiler, Piping, HRSG, Pressure Vessel, Static Equipment, Maintenance Work.
Facilities :
tube panel welding, automatic panel membrane, panel
bender, facing, swaging, expanding, finning, HT furnace,
RT chamber, etc.
Land Area：250,000㎡
Factory Area：50,000㎡

## Slide 5
RUKN 20224-2060:
In 2026 targeting PLTU Cfbio+CCS 12,2% of 443 GW demand.
MEMR Regulation No. 12/2023 _Article 5:
The utilization of Biomass Fuel for power plants as referred to in Article 2 for PLTU is implemented through Biomass Co-firing.
Biomass Co-firing as referred to in paragraph (1) is carried out by the Biomass Co-firing executors.
Government Policies
Electricity Supply Business Plan RUPTL 2025-2034:
One of the strategy to reduce greenhouse gas emissions through Accelerated Renewable Energy Development (ARED) is carried out with Biomass Co-firing.
PT PLN Persero
2. Indonesia Government & Utility Biomass Policies

## Slide 6: Current Status of Biomass Co-Firing in Indonesia
https://m.jpnn.com/news/manfaatkan-biomassa-pln-indonesia-power-berhasil-tingkatkan-produksi-energi-bersih, accessed 4/14/2026;16:06PM
https://www.facebook.com/plnnusantarapower/posts/sobat-nusantara-sepanjang-tahun-2025-pln-np-telah-membuktikan-bahwa-transisi-ene/1352205580039155/ , accessed 4/14/2026;16:06PM
Power Generated
1.101,59 GWh
Biomass Fuel Utilized
1.14 Mt
Power Generated
954.9 GWh
Biomass Fuel Utilized
0.97 Mt
Implemented in 25 CFPP
Press Release 6 March 20261
Press Release 7 January 20262
PLN Group 2025 Biomass Cofiring Implementation
2. Indonesia Government & Utility Biomass Policies
Chart: 2025 Biomass Cofiring Electricity Generated (GWh)
| Execution | RE Base | ARED
PLN IP | 1101.59
PLN NP | 954.9 | 0
RUPTL Target | 0 | 3871 | 11908
Actual generation remains well below the target Level

## Slide 7
Key Challenges (as in PLN RUPTL)
1. Technical & Operational Efficiency
Plant Efficiency Impact: Biomass co-firing can lead to a reduction in overall power plant efficiency and potential increases in BPP (Biaya Pokok Penyediaan / Basic Cost of Generation).
Technical Limits: Current implementation is successfully tested at a max 5% biomass co-firing
Future Requirements: 10%–20% ratio requires further testing and likely additional capital investment (CapEx) for boiler modifications and specialized handling systems.
2. Feedstock Supply & Sustainability
Security of Supply: The primary challenge is ensuring a consistent and high-volume feedstock supply to meet the massive scaling targets (10.2M tons/year).
Forest Conservation: Collaborating with the government and private sector to develop dedicated energy forests (industrial forests) to ensure biomass production does not lead to deforestation or disturb forest sustainability.
Business Eco-system Development: Necessity to prepare a robust business ecosystem, covering: Commercial Viability for suppliers, Regulatory clarity, Stakeholder cooperation.
3. Strategic Readiness
Technology Maturity: Aligning technology readiness across various power plant types (PLTU) to ensure co-firing can be implemented nationwide.
Logistical Infrastructure: Building the supply chain infrastructure required to move large volumes of biomass from production sites to power plants.
2. Indonesia Government & Utility Biomass Policies

## Slide 8
Biomass type
LHV, Moisture (Typical)
LHV: Lower Heating Value (as received base)
WOODY
Woody Chip
11.7 MJ/kg, 45%
Woody Pellet
16.7MJ/kg, 10%
Bark
7.4 MJ/kg, 52%
Pruned Wood
8.0 MJ/kg, 43%
Various shape
Easy to handle in
pellet form
WASTE
Waste Wood
13MJ/kg, 25%
Paper Sludge
2.6 MJ/kg, 64%
Including Chlorine and foreign matter such as nails etc.
High moisture Low Calorific value
Biomass Fuel Type
AGRICUL
TURAL
Coffee Grounds
8.8 MJ/kg, 60%
Bagasse
6.9 MJ/kg, 49%
Palm Waste
14.6 MJ/kg, 10%
High moisture
Rice Husk
14 MJ/kg, 11%
Rice Straw
13 MJ/kg, 15%
High moisture
Low Calorific value
Sawdust
11MJ/kg, 42%
3. Biomass (Co-)Firing Technologies

## Slide 9
IHI Development of Technology related for Biomass (Co-) firing.
The following items are the major considerations for biomass firing.
 | Items to be evaluated | Tools / Test Facilities
① Pulverizer | Grindability / Particle size Drying of wet biomass Material balance (heat / air flow) | - Labo. scale grindability Test facility - IHI Combustion Test facility - Ash Test facility for slagging/fouling - Ash Test Facility for corrosion - Flow simulation (CFD) - Actual burn at Power station
② Burner | Combustion performance - NOx/CO - Unburned biomass | 
③ Boiler | Thermal performance at heating elements Ash troubles (slagging/fouling/corrosion) GAH performance | 
IHI Combustion Test Facility
Ash Test Facility
Ash corrosion Test Facility
CFD
3. Biomass (Co-)Firing Technologies

## Slide 10
Modification for existing coal firing boiler / Newly construction
Various Co-firing rate
Achieved dedicated-firing with modification
IHI Biomass (Co-) firing Power Plants
Project | Output [MW] | (Co-)Firing rate [cal%] | Year
Many Ref. | - | 2~3 | 2005-Current
K | 149 | 8,25 | 2015
N | 110 | 30 | 2017
I | 149 | 25/42 | 2018/2023
O | 500 | 15 | 2020
T | 600 | 16 | 2022
S | 112 | 100 | 2022
A | 200 | 100 | 2023
NO | 700 | 15 | 2025
TK | 145 | 25 | 2025
IHI biomass (Co-)firing power plants in Japan
Received an order for the conversion to woody biomass fuel of boilers for power generation
-December 04, 2019-
IHI has received an order from Suzukawa Energy Center Co., Ltd. for the woody biomass conversion work of the thermal power plant. This project is for the woody biomass conversion project promoted by Suzukawa Energy Center and will be the first woody biomass conversion work in Japan at a PC-fired boiler. Commercial operation is scheduled in summer 2022.
Suzukawa Energy Center Power Station
https://www.ihi.co.jp/ihi/all_news/2018/resources_energy_environment/1190426_1616.html
https://www.ihi.co.jp/ihi/all_news/2019/resources_energy_environment/1190454_1591.html
Completed
3. Biomass (Co-)Firing Technologies

## Slide 11
Concept of (Co-)firing system
Coal
Feeder
Bio mass
Feeder
Boiler
Coal
Pulverizer
Mix-pulverizing system with coal pulverizer
◆ Current system
Co-firing rate : Max. a few % (in calorific value)
(Depends on pulverizer capacity )
Dedicated use pulverizing system for biomass (in particular wood pellet)
◆ Developed system
Co-firing rate : more than 15% (in calorific value)
Coal
Feeder
Bio mass
Feeder
Boiler
Coal
Pulverizer
Biomass
Pulverizer
Coal
4. Design Consideration for Biomass (Co-) Firing

## Slide 12
Grindability and Processing Capacity
One of the key issues of biomass firing is the difficulty in discharging the larger particle size of biomass from pulverizer to boiler.
In order to assist discharging the larger size of biomass IHI has developed the technology that this pulverized biomass (wood pellet) is exhausted by increasing flow velocity inside pulverizer equipped with “flow acceleration ring”.
Coal mono firing is acceptable by removing the ring.
Coal Pulverizer
Biomass Pulverizer
Large size biomass
requires higher terminal
velocity to be discharged
from mill.
・Biomass： 500μm-1mm
・Coal: 50μm
Flow Acceleration
Ring to increase velocity
4. Design Consideration for Biomass (Co-) Firing